## Slide 1: Midterm Presentation Estimating Brain Activation Patterns from EEG Data
Student: Gal Maman
Supervisor: Or Yair
Semester: Winter, 2017
Date: 20/12/2017
In Collaboration with: Dr. Danny Eitan

## Slide 2: Outline
Medical Background
Project Goals
Overview project process
Results
Conclusion
Future Work

## Slide 3: Medical Background
Brain injury is the leading cause of death in hospitalized children (Moreau et al., 2013).
Problem: Popular modalities for brain imaging such as MRI or CT are not always feasible or available at early stages of the illness.
Goal: Provide a system that can be applied at the bedside of critically-ill patients ,detect the neurological injury, aid in guiding therapy and improve outcomes.

## Slide 4
Solution: Electroencephalography (EEG) monitoring
Measures voltage fluctuations resulting from ionic current within the neurons of the brain.
Noninvasive, with the electrodes placed along the scalp.
Extremely high time resolution.
Challenges using EEG:
Noise - causes poor spatial resolution comparing to other methods.
Sensitive to movment – since the electrodes are located on the scalp, things like hair or curves in the scalp can damage the signal.

## Slide 5: Sub - Goals
Single Shot EEG classification
To complete
Electrodes reduction

## Slide 6: Overview project process System Diagram
Raw Data
Preprocessing
Statistical features extraction
Features processing
Classification
Classified Data

## Slide 7: Our Raw Data
Eleven healthy volunteers ranged in age from 7 to 16 years (median 12 years).
Five critically-ill patients ranged in age from 2.5 to 16 years (median 8.5 years); all with acute brain injury of various etiologies.
The stretchable electrode cap contained 68 EEG electrodes, The set-up consisted of three multi-modal sensory stimulation generators: visual, auditory and somatosensory.
The final data includes 200-1000 trials for each stimulus (9 stimulations) from every subject (16 subjects).

## Slide 8
Raw Data
Statistical features extraction
Features processing
Classification
Classified Data
Preprocessing
Overview project process System Diagram

## Slide 9: Preprocessing
The preprocessing was performed by Gilad and Ronen in the previous project and included these steps for each trial:
Convolution with BPF.
Cutting the signal in time so the length will be 0.5 msec.
Down sampling from 5kHz to 1kHz.
Disqualify trials (short-time windows) and electrodes.
At the end of the cleaning process we remained with 32 electrodes.

## Slide 10: Overview project process System Diagram
Raw Data
Features processing
Classification
Classified Data
Preprocessing
Statistical features extraction

## Slide 11: Statistical Features Extraction
A common statistical feature known to provide good results is the covariance.
Covariance matrix is SPD (symmetric and positive definite) matrix.
Cov(X) for trial X is defined by:
Another optional feature is the Gaussian kernel (kernel trick), which also gives us SPD matrices.
A kernel matrix for trial X is defined by:

## Slide 12: Overview project process System Diagram
Raw Data
Classification
Classified Data
Preprocessing
Statistical features extraction
Features processing

## Slide 13: Dimensionality reduction algorithms
PCA:
Linear method, based on the eigenvectors and eigenvalues of the data set.
Diffusion Maps:
Nonlinear method. The algorithm includes the following steps:
Building a weighted graph based on a pairwise weight function k:
Definition of a Markov process on the graph.
Nonlinear mapping of the samples, using SVD.
t-SNE:
Also a nonlinear method. t-SNE is mostly suited for the visualization of high-dimensional datasets, i.e. reduction to two or three dimensions

## Slide 14: Riemannian Geometry
The space of SPD matrices p(n) is a differentiable Riemannian Manifold ʍ.
The Riemannian Geodesic Distance is defined by:
In order to use popular classification algorithms we first need to project our matrices into an Euclidean tangent space.
ʍ
How will we choose Euclidean tangent space?
How will we project our matrices?

## Slide 15
ʍ
For each point P ∈ P(n), we can define a tangent space composed by the set of tangent vectors at P. Each SPD matrix (covariance of a trial) is then mapped into this tangent space by this formula:
Then we can us this approximation:
At the previous project, we used a tangent space located at the geometric mean of the whole set of trials.

## Slide 16
Results of PCA, while our center is the Riemannian mean of whole set of trials.
Data set: all healthy subjects, all stimulus:

## Slide 17: Schild’s Ladder (Parallel Transport)
At this approach, first we will calculate the Riemannian mean for each subject.
ʍ
After transferring all of the trials, we will project them on a tangent space located at our chosen mean, just as in the standard method.
Then, using parallel transport, we will locate all SPD matrices (which present our trials) around our chosen mean, in a way that will preserve the original structure, by using Riemannian matric properties.
Then we calculate Riemannian mean over all Riemannian means.
How will we transfer the matrices wisely?

## Slide 18
First, we will review the parallel definition of vectors in the Riemannian matric:
)
The projection:
Let be SPD matrix of trial j in subject i.
Let be the Riemannian mean of subject I, and let be our chosen mean.
?

## Slide 19
In the Euclidean space, we would use simple parallelogram properties:
In the Riemannian space, we can use the parallel definitions from the last slide:

## Slide 20
Results of PCA, while our center is the Riemannian mean all the Riemannian means.
Data set: all healthy subjects, all stimulus:

## Slide 21
Parallel transport – before and after
We can see that while without PT, subject 11 is apart from the other subjects, after PT all the subjects are aligned, and we can see separation by stimulations. Note that all the mixed stimulations are with similar character (visual, auditory and somatosensory).

## Slide 22: Overview project process System Diagram
Raw Data
Classified Data
Preprocessing
Statistical features extraction
Features processing
Classification

## Slide 23: SVM Support Vector Machines
A method used for classification and regression analyses.
SVM represent the data set as points in space, mapped so that samples with different labels are divided by a clear. New samples are then mapped into that same space and ascribed to a label based on which side of the gap they fell.

## Slide 24: Overview project process System Diagram
Raw Data
Classified Data
Preprocessing
Statistical features extraction
Features processing
Classification

## Slide 25: Results Confusion Matrix
Data used: 50 trials from each stimulation, from all healthy subjects (After PCA)
Code | system | details
1 | Somatosensory | right arm
2 | Somatosensory | left arm
3 | Visual | light flash
11 | Auditory | Frequent tone
12 | Auditory | rare tone
13 | Auditory | sham word 1
14 | Auditory | Subject own name
15 | Auditory | sham word
16 | Auditory | Sham word

## Slide 26: A series of tests performed on subjects C01, C02 stimulus 1, 3, 14

## Slide 27: A series of tests performed on subjects C01, C02 stimulus 1, 3, 14

## Slide 28: A series of tests performed on subjects C04,C05,C06,S01,S02,S04 stimulus 2, 3, 11,14

## Slide 29: A series of tests performed on subjects C03, C04,C05,S01,S02,S04 stimulus 2, 3, 11,14

## Slide 30: A series of tests performed on subjects C03, C04,C05,S01,S02,S04 stimulus 2, 3, 11,14

## Slide 31: A series of tests performed on subjects C03, C04,C05,S01,S02,S04 stimulus 2, 3, 11,14

## Slide 32: Conclusion
Repeat the project goal in other words
  Have you achieved the goal? (if not, this is ok and you have to explain why)
Summarize your results
Emphasize original contribution

## Slide 33: Future Work
Suggestions for continuation of your work

## Slide 34: References
TALMON, R; et al.‪ Diffusion Maps for Signal Processing: A Deeper Look at Manifold-Learning Techniques Based on Kernels and Graphs.‪ IEEE Signal Processing Magazine.‪ 30, 4, 75, July 2013.‪ ISSN: 10535888.‪‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬
Alexandre Barachant ; et al. Multiclass Brain–Computer Interface Classification by Riemannian Geometry.‪ IEEE Transactions on Biomedical Engineering, Biomedical Engineering, IEEE Transactions on, IEEE Trans. Biomed. Eng.‪ USA, 4, 920, 2012.‪ ISSN: 1558-2531.‪‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬