## Slide 1: Final Presentation Estimating Brain Activation Patterns from EEG Data
Student: Gal Maman
Supervisor: Or Yair
Semester: Winter, 2017
Date: 08/05/2018
In Collaboration with: Dr. Danny Eitan

## Slide 2: Outline
Medical Background
Project Goals
Overview project process
Results
Conclusions and Future Work

## Slide 3: Medical Background
Goal:
A system that:
Can be applied at the bedside of critically-ill patients.
Detect neurological injury.
Aid in guiding therapy and improve outcomes.
Problem:
Popular modalities for brain imaging are not always feasible or available at early stages of the illness.
Solution:
Research brain activity using Electroencephalography (EEG) monitoring.
Acute brain injury is a common cause of death among children.

## Slide 4: Objectives
Single shot EEG classification
Detect functional areas
Spatial sub-sampling

## Slide 5: Our Raw Data
11 healthy volunteers ranged in age from 7 to 16 years.
5 critically-ill patients ranged in age from 2.5 to 16 years; all with various brain injuries.
Chart: 
| 2.5 | 6.5-7 | 8.5-10 | 12 | 13-13.5 | 15-16
Sick | 1 | 1 | 1 | 0 | 1 | 1
Healthy | 0 | 2 | 2 | 3 | 1 | 2
Age range
Number of subjects

## Slide 6: Our Raw Data
The stretchable electrode cap contained 64 EEG electrodes.

## Slide 7: Our Raw Data
The set-up consists of three multi-modal sensory stimulation generators: somatosensory, auditory and visual.
The final data includes 200-1000 trials for each stimulus (9 stimulations) from every subject (16 subjects).
2
6
1

## Slide 8: Overview Scheme Process System Diagram
Raw Data
Preprocessing
Statistical Features Extraction
Features Processing
Classification
Classified Data

## Slide 9: Overview Scheme Process System Diagram
Raw Data
Statistical Features Extraction
Features Processing
Classification
Classified Data
Preprocessing
BP filter.
Down sampling.
Disqualify trials and electrodes.
 32 electrodes

## Slide 10: Overview Scheme Process System Diagram
Raw Data
Features Processing
Classification
Classified Data
Preprocessing
Statistical Features Extraction

## Slide 11: Statistical Features Extraction
Let be a trial with channels, each channel with 500 samples in time.
Trial :
Normalization: each channel is normalized to zero mean and unit standard deviation.
Previous work suggest using covariance matrices as features along with a Riemannian geometry framework. Specifically, we use the Riemannian manifold of SPD matrices.
By definition:

## Slide 12: Overview Scheme Process System Diagram
Raw Data
Classification
Classified Data
Preprocessing
Statistical Features Extraction
Features Processing

## Slide 13: Riemannian Geometry
Let be the Riemannian Manifold of all SPD matrices.
Let be covariance matrices created from different trials.
The Riemannian Geodesic distance is defined by:
We can approximate the Riemannian distance by embedding the SPD matrices in the tangent space .

## Slide 14
Let be a set of SPD matrices, and let be their Riemannian mean:
Let be a tangent space defined by a set of tangent vectors at
Traditional approach: Project all matrices to the tangent plane located at the Riemannian mean of the entire set of SPD matrices.

## Slide 15
Example: 3 healthy subjects, 3 stimulations

## Slide 16
Suggested approach: Parallel Transport
Let and be the Riemannian mean of and .
Project the covariance matrices into the tangent plane
Apply PT to along the geodesicgeodesic path between and
Closed form expression:
Where

## Slide 17
Example: 3 healthy subjects, 3 stimulations

## Slide 18
Without PT With PT

## Slide 19: Rotation Using PCA
We have noticed that even though PT locates all the subjects around the same center, they remain with their original angle, which creates “X” shape:

## Slide 20: Rotation Using PCA
We have noticed that even though PT locates all the subjects around the same center, they remain with their original angle, which creates “X” shape:

## Slide 21: Rotation Using PCA
Since usually all the subjects have the same main components, we can use PCA to transfer them to the same coordinate system.
After performing PCA, the stimulations will either be aligned, or opposite with 180 degrees.
We chose to rotate according to the acute angle

## Slide 22
Without rotation With rotation

## Slide 23
Without rotation With rotation

## Slide 24: Overview Scheme Process System Diagram
Raw Data
Classified Data
Preprocessing
Statistical Features Extraction
Features Processing
Classification

## Slide 25: Classification Methods
We used different algorithms such as SVM, Trees etc.
We classified using “leave one out” method, i.e. we trained the classifier with all the subjects besides one, and tested the classifier on that subject.

## Slide 26: Overview Scheme Process System Diagram
Raw Data
Classified Data
Preprocessing
Statistical Features Extraction
Features Processing
Classification

## Slide 27: Single Shot EEG classification Results 3 Healthy subjects Stimulus 1,3,14

## Slide 28: Single Shot EEG classification Results 8 Healthy subjects Stimulus 1,3,11

## Slide 29: Linear SVM Classifier

## Slide 30
Without rotation With rotation

## Slide 31
Without rotation With rotation

## Slide 32: Linear SVM Classifier

## Slide 33: 5 Sick Subjects Stimulus 1,3,14

## Slide 34: Healthy Subjects vs Sick Subjects 2 Healthy subjects, 1 sick subject Stimulus 2,3,11

## Slide 35: Spatial Sub-Sampling
Choose stimulations
Choose initial electrodes
Pick a set of subjects
Sub-sample

## Slide 36: Spatial Sub-Sampling Results

## Slide 37: Spatial Sub-Sampling Results

## Slide 38: Spatial Sub-Sampling Results

## Slide 39: Conclusion
We managed to reach good classification performance using PT and rotation, especially with stimulations from different functional areas.
We proved that the data can be sub-sampled (2-5 electrodes).

## Slide 40: Future Work
Publish our conclusions so far.
Develop an algorithm that chooses the electrodes that best classify the data.
Use kernel matrix (SPD) instead of covariance, for example:
Deepen analysis in frequency domain

## Slide 41
Time Domain Frequency Domain

## Slide 42: Subject S02, 3 Stimulus
Time Domain Frequency Domain

## Slide 43: References
TALMON, R; et al.‪ Diffusion Maps for Signal Processing: A Deeper Look at Manifold-Learning Techniques Based on Kernels and Graphs.‪ IEEE Signal Processing Magazine.‪ 30, 4, 75, July 2013.‪ ISSN: 10535888.‪‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬
Alexandre Barachant ; et al. Multiclass Brain–Computer Interface Classification by Riemannian Geometry.‪ IEEE Transactions on Biomedical Engineering, Biomedical Engineering, IEEE Transactions on, IEEE Trans. Biomed. Eng.‪ USA, 4, 920, 2012.‪ ISSN: 1558-2531.‪‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬‬